## Slide 1
Project Task 2
CodeAlpha
CASE STUDY
Drug Formulation:
Immediate-Release Tablet
Paracetamol (Acetaminophen) 500 mg Compressed Tablet
Formulation Process • Excipients • Stability • Challenges
Pharmaceutics | Solid Oral Dosage Forms

## Slide 2
Why the Tablet Dosage Form?
Compressed tablets remain the most widely used dosage form in oral drug delivery
Accurate Dosing
Uniform drug content per unit, manufactured under strict weight and content-uniformity control.
Manufacturing Efficiency
High-speed rotary presses enable large-scale, low-cost production with excellent reproducibility.
Stability & Handling
Low moisture content and compact form give tablets good chemical and physical shelf-life.
Patient Convenience
Easy to package, transport, identify, and self-administer without specialized equipment.
Drug Formulation Case Study | Immediate-Release Tablet
2

## Slide 3
Formulation Process — Wet Granulation Route
The most common method for tablets with poor flow/compressibility, such as paracetamol
1
Dispensing &
Mixing
2
Wet
Granulation
3
Drying
4
Milling &
Sizing
5
Blending with
Lubricant
6
Compression
7
Coating &
Packaging
Key Process Notes
Granulation binds fine API and diluent powders into free-flowing granules, improving compressibility.
Drying (tray or fluid-bed) reduces moisture to the target LOD, preventing capping and sticking later.
Lubricant is blended briefly at the end — over-blending weakens tablet hardness and delays disintegration.
In-process checks: granule size distribution, LOD, blend uniformity, tablet weight, hardness, friability.
Drug Formulation Case Study | Immediate-Release Tablet
3

## Slide 4
Excipients Used in the Formulation
Representative tablet formula (per 500 mg dose unit)
Category | Excipient | Function | % w/w
Active | Paracetamol | Therapeutic agent (analgesic / antipyretic) | 71.4%
Diluent | Microcrystalline Cellulose (Avicel PH101) | Bulking agent; improves compressibility | 15.0%
Binder | Povidone (PVP K30) | Binds particles into granules for strength | 3.0%
Disintegrant | Sodium Starch Glycolate | Promotes rapid tablet breakup in fluid | 5.0%
Glidant | Colloidal Silicon Dioxide | Improves powder flow into the die | 0.5%
Lubricant | Magnesium Stearate | Reduces friction; prevents sticking to punches | 1.0%
Coating | Opadry (HPMC-based film) | Aids swallowing, masks taste, protects from moisture | 4.1%
Drug Formulation Case Study | Immediate-Release Tablet
4

## Slide 5
Stability Factors
Conditions monitored across accelerated (40°C/75% RH) and long-term stability studies
Temperature
Elevated heat accelerates hydrolysis of paracetamol to p-aminophenol; controlled storage limits degradation.
Humidity / Moisture
Moisture ingress softens granules, causes caking, and can hydrolyze the API — desiccant packaging is used.
Light Exposure
Photo-sensitive degradation is minimized with opaque film coating and light-protective blister foil.
Excipient Compatibility
Reducing sugars and certain lubricants can react with the API; compatibility studies screen excipients early.
Oxidation
Trace oxidative impurities are limited using antioxidants and inert (nitrogen-purged) processing where needed.
Packaging Integrity
Alu-Alu or PVC/PVdC blisters provide a moisture and oxygen barrier over the shelf-life period.
Drug Formulation Case Study | Immediate-Release Tablet
5

## Slide 6
Formulation Challenges & Mitigations
Common Challenges
Paracetamol has poor natural compressibility and tends toward capping/lamination.
High drug loading (>70%) leaves limited room for functional excipients.
Moisture-sensitive API risks hydrolysis during aqueous granulation.
Batch-to-batch variability in granule flow affects weight uniformity.
Scale-up from lab press to production tooling can shift hardness/dissolution.
Mitigation Strategies
Use MCC as a plastic-deforming diluent to improve binding and reduce capping.
Optimize binder concentration and granulation endpoint via in-process monitoring.
Prefer non-aqueous or controlled-moisture granulation; tight drying LOD limits.
Apply design of experiments (DoE) to lock in robust process parameters.
Bridge scale-up with compressibility/compactibility studies before validation batches.
Drug Formulation Case Study | Immediate-Release Tablet
6

## Slide 7
Key Takeaways
7
Core process
steps
6
Excipient
categories
40°C/75%RH
Accelerated
stability test
A well-designed tablet formulation balances functional excipients against a high drug load to achieve consistent hardness, disintegration, and dissolution.
Wet granulation remains the reliable route for poorly compressible actives like paracetamol, provided moisture and blending are tightly controlled.
Stability is engineered in from the start — through excipient compatibility, film coating, and moisture-barrier packaging — not tested in as an afterthought.
Proactive risk assessment (DoE, in-process controls) turns scale-up and manufacturing challenges into predictable, manageable variables.
Drug Formulation Case Study | Immediate-Release Tablet
7